## Slide 1
ASTRODIG LLC
AstroDig LLC - RegolithWorks 5.0 - Ground Campaign Overview
2017-08-15 | Internal | 1
Capture-Cartridge Testing
Defined ground evidence before the next mission decision.
GROUND DEVELOPMENT
Notes: Capture-Cartridge Testing Defined ground evidence before the next mission decision.

## Slide 2
ASTRODIG LLC
The decision problem
2017-08-15 | Internal | 2
01
Changing inputs and configurations make results difficult to compare.
02
Current development risk: material escape.
03
Capture efficiency is limited to controlled test materials.
Notes: Changing inputs and configurations make results difficult to compare. Current development risk: material escape. Capture efficiency is limited to controlled test materials.

## Slide 3
ASTRODIG LLC
A controlled campaign boundary
2017-08-15 | Internal | 3
Prefer contained recovery over an open collection path.
Scope: Controlled ground-test use.
Accepted evidence and unresolved dependencies stay separate.
Notes: Prefer contained recovery over an open collection path. Scope: Controlled ground-test use. Accepted evidence and unresolved dependencies stay separate.

## Slide 4
ASTRODIG LLC
Containment and safe control
2017-08-15 | Internal | 4
1
Containment: The test cartridge shall remain closed throughout the collection sequence.
2
Pressure envelope: The chamber controller shall inhibit a sequence outside the approved pressure envelope.
3
Thermal limit: The heater controller shall stop heating when the configured temperature limit is reached.
4
Power interlock: Actuator power shall require an independent enabled interlock.
5
Emergency stop: An emergency-stop request shall supersede an active extraction command.
Notes: Containment: The test cartridge shall remain closed throughout the collection sequence. Pressure envelope: The chamber controller shall inhibit a sequence outside the approved pressure envelope. Thermal limit: The heater controller shall stop heating when the configured temperature limit is reached. Power interlock: Actuator power shall require an independent enabled interlock. Emergency stop: An emergency-stop request shall supersede an active extraction command.

## Slide 5
ASTRODIG LLC
Evidence and configuration
2017-08-15 | Internal | 5
Sample custody: Every sample container shall carry a unique identifier linked to its run.
Blank control: Each material campaign shall include an empty-cartridge blank run.
Mass accounting: The run record shall include input, recovered, retained, and unaccounted mass.
Time synchronization: Controller and instrument events shall share a synchronized run clock.
Telemetry continuity: The controller shall flag any telemetry gap longer than two seconds.
Notes: Sample custody: Every sample container shall carry a unique identifier linked to its run. Blank control: Each material campaign shall include an empty-cartridge blank run. Mass accounting: The run record shall include input, recovered, retained, and unaccounted mass. Time synchronization: Controller and instrument events shall share a synchronized run clock. Telemetry continuity: The controller shall flag any telemetry gap longer than two seconds.

## Slide 6
ASTRODIG LLC
Recovery and acceptance
2017-08-15 | Internal | 6
1
Configuration control: The run header shall record controller, cartridge, and sensor revisions.
2
Calibration freshness: Mass and temperature measurements shall use current approved calibrations.
3
Recovery restart: Restart after an abort shall require a new pre-run checklist.
4
Data export: Exported run data shall include units, channel names, and quality flags.
5
Operator authority: Only an authorized operator shall acknowledge a safety hold.
Notes: Configuration control: The run header shall record controller, cartridge, and sensor revisions. Calibration freshness: Mass and temperature measurements shall use current approved calibrations. Recovery restart: Restart after an abort shall require a new pre-run checklist. Data export: Exported run data shall include units, channel names, and quality flags. Operator authority: Only an authorized operator shall acknowledge a safety hold.

## Slide 7
ASTRODIG LLC
From inputs to a reviewable result
2017-08-15 | Internal | 7
01
Register configuration and inputs
02
Run approved reference checks
03
Execute bounded campaign
04
Review evidence and discrepancies
05
Accept or hold the next configuration
Notes: Register configuration and inputs Run approved reference checks Execute bounded campaign Review evidence and discrepancies Accept or hold the next configuration

## Slide 8
ASTRODIG LLC
Three engineering uses
2017-08-15 | Internal | 8
01
Mission trade study: Compare candidate operating assumptions without asserting resource recoverability.
02
Payload verification campaign: Link a controlled test sequence to acceptance evidence and configuration identity.
03
Readiness review: Identify open discrepancies and distinguish accepted evidence from unresolved dependencies.
Notes: Mission trade study: Compare candidate operating assumptions without asserting resource recoverability. Payload verification campaign: Link a controlled test sequence to acceptance evidence and configuration identity. Readiness review: Identify open discrepancies and distinguish accepted evidence from unresolved dependencies.

## Slide 9
ASTRODIG LLC
What teams must bring
2017-08-15 | Internal | 9
01
approved input or test-material specification
02
named technical reviewer
03
configuration-controlled reference case
Notes: approved input or test-material specification named technical reviewer configuration-controlled reference case

## Slide 10
ASTRODIG LLC
Where the evidence stops
2017-08-15 | Internal | 10
Capture efficiency is limited to controlled test materials.
Not in scope: Flight qualification, asteroid resource certification, commercial mining, or mission approval.
A ground-development release is not flight qualification.
Notes: Capture efficiency is limited to controlled test materials. Not in scope: Flight qualification, asteroid resource certification, commercial mining, or mission approval. A ground-development release is not flight qualification.

## Slide 11
ASTRODIG LLC
Define the reference case
2017-08-15 | Internal | 11
Available to contracted engineering teams through a scoped technical review.
Request a technical review through media@astrodig.example; define the reference case and acceptance evidence before campaign access.
Notes: Available to contracted engineering teams through a scoped technical review. Request a technical review through media@astrodig.example; define the reference case and acceptance evidence before campaign access.